## Slide 1: Computer Network Security
Mrs. M. Lalli
Assistant Professor
Department of Computer Science
Bharathidasan University
Trichy

## Slide 2: Computer Networks
Computer network connects two or more autonomous computers.
The computers can be geographically located anywhere.

## Slide 3: LAN, MAN & WAN
Network in small geographical Area (Room, Building or a Campus) is called LAN (Local Area Network)
Network in a City is call MAN (Metropolitan Area Network)
Network spread geographically (Country or across Globe) is called WAN (Wide Area Network)

## Slide 4: Applications of Networks
Resource Sharing
  Hardware (computing resources, disks, printers)
  Software (application software)
Information Sharing
  Easy accessibility from anywhere (files, databases)
  Search Capability (WWW)
Communication
  Email
  Message broadcast
Remote computing
Distributed processing (GRID Computing)
Introduction to Computer Networks

## Slide 5: Network Topology
The network topology defines the way in which computers, printers, and other devices are connected. A network topology describes the layout of the wire and devices as well as the paths used by data transmissions.

## Slide 6: Bus Topology
Commonly referred to as a linear bus, all the devices on a bus topology are connected by one single cable.
Introduction to Computer Networks

## Slide 7: Star & Tree Topology
The star topology is the most commonly used architecture in Ethernet LANs.
When installed, the star topology resembles spokes in a bicycle wheel.
Larger networks use the extended star topology also called tree topology. When used with network devices that filter frames or packets, like bridges, switches, and routers, this topology significantly reduces the traffic on the wires by sending packets only to the wires of the destination host.
Introduction to Computer Networks

## Slide 8: Ring Topology
A frame travels around the ring, stopping at each node. If a node wants to transmit data, it adds the data as well as the destination address to the frame.
The frame then continues around the ring until it finds the destination node, which takes the data out of the frame.
  Single ring – All the devices on the network share a single cable
  Dual ring – The dual ring topology allows data to be sent in both directions.

## Slide 9: Mesh Topology
The mesh topology connects all devices (nodes) to each other for redundancy and fault tolerance.
It is used in WANs to interconnect LANs and for mission critical networks like those used by banks and financial institutions.
Implementing the mesh topology is expensive and difficult.

## Slide 10: Network Components
Physical Media
Interconnecting Devices
Computers
Networking Software
Applications
Introduction to Computer Networks

## Slide 11: Networking Media
Networking media can be defined simply as the means by which signals (data) are sent from one computer to another (either by cable or wireless means).
Introduction to Computer Networks

## Slide 12: Networking Devices
HUB, Switches, Routers, Wireless Access Points, Modems etc.
Introduction to Computer Networks

## Slide 13: Computers: Clients and Servers
In a client/server network arrangement, network services are located in a dedicated computer whose only function is to respond to the requests of clients.
The server contains the file, print, application, security, and other services in a central computer that is continuously available to respond to client requests.

## Slide 14: Networking Protocol: TCP/IP

## Slide 15: Applications
E-mail
Searchable Data (Web Sites)
E-Commerce
News Groups
Internet Telephony (VoIP)
Video Conferencing
Chat Groups
Instant Messengers
Internet Radio

## Slide 16: OSI Reference Model: 7 Layers
OSI Model

## Slide 17: Open Systems Interconnection
OSI Reference model
  Layer 7 application
  Layer 6 presentation
  Layer 5 session
  Layer 4 transport
  Layer 3 network
  Layer 2 data link
  Layer 1 physical
File
Transmission Medium
File
Sender
Receiver
File
Each file
is divided
into
packets
The received
frame is then
unpacked
in the
opposite order
Each Packet
will
then be
Encapsulated
with
PROTOCOLS
The protocols
Will be added
systematically
Layer
By layer
The encapsulated
Packet is called a frame

## Slide 18: Services Performed at Each Layer
  Layer 7 application
  Layer 6 presentation
  Layer 5 session
  Layer 4 transport
  Layer 3 network
  Layer 2 data link
  Layer 1 physical
  Identification, authentication
  Format conversion
  Set-up coordinate conversation
  Ensures error-free transfer
  Routing of data through network
  Error control and synchronisation
  Placing signals on the carrier

## Slide 19: Examples of protocols
  Layer 7 application
  Layer 6 presentation
  Layer 5 session
  Layer 4 transport
  Layer 3 network
  Layer 2 data link
  Layer 1 physical
  E-mail, Web browser, Directory
  POP, SMTP, FTP, HTTP, DNS
  Sockets
  TCP
  IP
  PPP, Ethernet, Token ring
  100baseT

## Slide 20: Encapsulation
Application
Presentation
Session
Transport
Network
Data Link
Physical
data
Device 1
Device 2
data
H6
T6
data
H5
T5
data
H4
T4
(packet)
H3
data
T3
H2
data
T2
H1
data
T1
carrier
FRAME
Application
Presentation
Session
Transport
Network
Data Link
Physical
A typical frame
Destination
Address
Source
Address
Data
Padding
CRC
Preamble
FRAME
FRAME
FRAME
(Packet)

## Slide 21
OSI layers

## Slide 22: Remembering the 7 Layers
7 - Application All
6 - Presentation People
5 - Session Seem
4 - Transport To
3 - Network Need
2 - Data Link Data
1 - Physical Processing

## Slide 23: Error Checking Methods
Parity bit check
Check sum
* data transmitted in blocks, each block added to give a total – checksum
* used in X Modem protocol
Cycle redundancy check

## Slide 24: OSI & TCP/IP Models
TCP/IP Model

## Slide 25: TCP/IP Model
TCP/IP Model
Application Layer
Application programs using the network
Transport Layer (TCP/UDP)
Management of end-to-end message transmission,
error detection and error correction
Network Layer (IP)
Handling of datagrams : routing and congestion
Data Link Layer
Management of cost effective and reliable data delivery,
access to physical networks
Physical Layer
Physical Media

## Slide 26: TCP/IP protocol stack

## Slide 27: TCP/IP Reference Model
Application
Transport
Internet
Network Access (Host-to-network)
Layer
HTTP
TELNET
FTP
SMTP
SNMP
Protocols
TCP
UDP
IP
ICMP
ETHERNET
PACKET RADIO

## Slide 28: Examples of Communication Systems

## Slide 29
Examples of Communication Systems
- E-mail
- Voice Mail - Fax
- Smart Phone - Instant Messaging
- Telecommuting - Video-conferencing
- Groupware - Telephony
- E-Commerce - The Internet
Bulletin board system - The Web
- Global positioning system

## Slide 30: Transmitting and Receiving in Communication Systems
Communication concepts
(transmission of data, protocols and handshaking, networks, LANs and WANs,Topologies, Network Access Methods)
Network Hardware
(NICs, Servers, Routers and Switches, Bridges and gateways, Hubs, Transmission media
Network Software
NOSs, Network Operating System Tasks, Logon and Logoff Procedures, Intranets and Extranets

## Slide 31: Communication Concepts
Any transmission May be:
analog or digital
Serial or parallel

## Slide 32: Serial Transmission
Data is transmitted, on a single channel, one bit at a time one after another
- Much faster than parallel because of way bits processed (e.g. USB drives)
Sender transmitted
Receiver received
1
0
1
0
0
1
1
0

## Slide 33: Parallel Transmission
Receiver received
each bit has it’s own piece of wire along which it travels
- often used to send data to a printer
Sender transmitted
All bits are sent simultaneously
1
0
0
1
1
0
0
1

## Slide 34: Why Not use Parallel Instead of serial?
Due to inconsistencies on channels data arrives at different times
Because of the way it is transmitted packet switching cannot be used
The above two points makes parallel slower than serial and requires higher bandwidth.
Parallel transmissions are rarely used anymore

## Slide 35: Synchronous Vs AsynchronousTransmissions
Synchronous Transmission
all data sent at once and no packet switching
Asynchronous Transmission
Uses stop/ start bits
most common type of serial data transfer
Allows packet switching
Allows sharing of bandwidth (i.e. talk on phone while another person is using internet)

## Slide 36: Transmission Direction
- simplex: One direction only

## Slide 37: Half Duplex Transmission
half duplex: Both directions but only one direction at a time

## Slide 38: Full Duplex Transmission
full duplex: send and receive both directions at once

## Slide 39: Bridge
Large networks can be separated into two or more smaller networks using a bridge.
This is done to increase speed and efficiency.
This type of network is called a segmented LAN and has largely been superseded by the use of switches which can transfer data straight to a computer and thus avoid bottleneck jams which bridges were designed to fix.
Bridge
Notes: Devives that connect local area networks
If a BUS or ring then a Gateway needs to be used

## Slide 40: Gateway
Often used to connect a LAN with a WAN. Gateways join two or
More different networks together.
Gateway

## Slide 41: Security

## Slide 42: In 1980 a computer cracked a 3-character password within one minute.
DID YOU KNOW?
In 2004 a computer virus infected 1 million computers within one hour.
In 1999 a team of computers cracked a 56-character password within one day.

## Slide 43: Objectives
Why we secure information?
What are the vulnerabilities?
How to secure information?

## Slide 44
Attack Sophistication vs. Intruder Technical Knowledge
High
Low
1980
1985
1990
1995
2000
password guessing
self-replicating code
password cracking
exploiting known vulnerabilities
disabling audits
back doors
hijacking
sessions
sweepers
sniffers
packet spoofing
GUI
automated probes/scans
denial of service
www attacks
Tools
Attackers
Intruder
Knowledge
Attack
Sophistication
“stealth” / advanced scanning techniques
burglaries
network mgmt. diagnostics
distributed
attack tools
Cross site scripting
Staged attack

## Slide 45: Security Objectives
Confidentiality: prevent/detect/deter improper disclosure of information
Integrity: prevent/detect/deter improper modification of information
Availability: prevent/detect/deter improper denial of access to services

## Slide 46: Definition of IS
Information security means protecting information and information systems from unauthorized access (That is modification, inspection, recording or destruction).
Information Security is interrelated with the common goals of protecting the confidentiality, integrity and availability of information.

## Slide 47: Friends and enemies: Alice, Bob, Trudy
well-known in network security world
Bob, Alice (lovers!) want to communicate “securely”
Trudy (intruder) may intercept, delete, add messages
secure
sender
secure
receiver
channel
data, control messages
data
data
Alice
Bob
Trudy
secure
sender

## Slide 48: Attacks
An attack is any action that violates security.
To analyze the security, it will depend upon the Three factors they are,
Vulnerability – Weakness in the security system
Threats – Set of circumstances that has
potential to cause loss or harm
Controls – Reduces the vulnerability

## Slide 49: Types of Vulnerabilities
Hardware Vulnerabilities – Physical damage
Software Vulnerabilities – Deletion, modification & theft
Example :(Logic Bomb, Salami Attack, Trojan horse )
Data Vulnerabilities – Confidentiality, Integrity and Availability

## Slide 50: Military Example
Confidentiality: target coordinates of a missile should not be improperly disclosed
Integrity: target coordinates of missile should be correct
Availability: missile should fire when proper command is issued

## Slide 51: Commercial Example
Confidentiality: patient’s medical information should not be improperly disclosed
Integrity: patient’s medical information should be correct
Availability: patient’s medical information can be accessed when needed for treatment

## Slide 52: Fourth Objective
Securing computing resources: prevent/detect/deter improper use of computing resources
  Hardware
  Software
  Data
  Network

## Slide 53: Achieving Security
Policy
  What to protect?
Mechanism
  How to protect?
Assurance
  How good is the protection?

## Slide 54: Security Policy
Organizational
Policy
Computerized
Information System
Policy

## Slide 55: Security Mechanism
Prevention
Detection
Tolerance/Recovery

## Slide 56
Types of Attacks (1)
Interruption – an asset is destroyed, unavailable or unusable (availability)
Interception – unauthorized party gains access to an asset (confidentiality)
Modification – unauthorized party tampers with asset (integrity)
Fabrication – unauthorized party inserts counterfeit object into the system (authenticity)
Denial – person denies taking an action (authenticity)

## Slide 57
Types of Attacks (2)
Passive attacks:
  Eavesdropping
  Monitoring
Active attacks:
  Masquerade – one entity pretends to be a different entity
  Replay – passive capture of information and its retransmission
  Modification of messages – legitimate message is altered
  Denial of service – prevents normal use of resources

## Slide 58: Malicious Attacks
Method: skills, knowledge, tools, information, etc.
Opportunity: time and access
Motive: reason to perform the action

## Slide 59: Computer Criminals
Amateurs: regular users, who exploit the vulnerabilities of the computer system
  Motivation: easy access to vulnerable resources
Crackers: attempt to access computing facilities for which they do not have the authorization
  Motivation: enjoy challenge, curiosity
Career criminals: professionals who understand the computer system and its vulnerabilities
  Motivation: personal gain (e.g., financial)

## Slide 60: Methods of Defense
Prevent: block attack
Deter: make the attack harder
Deflect: make other targets more attractive
Detect: identify misuse
Tolerate: function under attack
Recover: restore to correct state

## Slide 61: Encryption and Decryption
Encryption : (Encoding a message)
Original message (or) Plain Text is converted to cipher text
Decryption: (Decoding a message)
Cipher text is converted to Plain text
Plain Text Cipher Text Original Msg
Encryption
Decryption

## Slide 62: Encryption Technique ( Caesar Cipher)
Ci = E(pi) = Pi + 3
Plain Text = A B C D E F G H I J K L M N O . .
CipherText = d e f g h i j k l m n o p q r . .

## Slide 63: Example for caesar cipher
The Original Message is,
“TREATY IMPOSSIBLE”
The encrypted message is,
T R E A T Y I M P O S S I B L E
w u h d w b l p s r v v l e o h

## Slide 64: Firewalls
Firewalls control the flow of network traffic
Firewalls have applicability in networks where there is no internet connectivity
Firewalls operate on number of layers
Can also act as VPN gateways
Active content filtering technologies

## Slide 65: Firewall Environments
There are different types of environments where a firewall can be implemented.
Simple environment can be a packet filter firewall
Complex environments can be several firewalls and proxies

## Slide 66: Intranets
An intranet is a network that employs the same types of services, applications, and protocols present in an Internet implementation, without involving external connectivity
Intranets are typically implemented behind firewall environments.

## Slide 67: Intranets

## Slide 68: Extranets
Extranet is usually a business-to-business intranet
Controlled access to remote users via some form of authentication and encryption such as provided by a VPN
Extranets employ TCP/IP protocols, along with the same standard applications and services

## Slide 69: Type is Firewalls
Firewalls fall into four broad categories
Packet filters
Circuit level
Application level
Stateful multilayer

## Slide 70: Packet Filter
Work at the network level of the OSI model
Each packet is compared to a set of criteria before it is forwarded
Packet filtering firewalls is low cost and low impact on network performance

## Slide 71: Packet Filtering

## Slide 72: Circuit level
Circuit level gateways work at the session layer of the OSI model, or the TCP layer of TCP/IP
Monitor TCP handshaking between packets to determine whether a requested session is legitimate.

## Slide 73: Circuit Level

## Slide 74: Application Level
Application level gateways, also called proxies, are similar to circuit-level gateways except that they are application specific
Gateway that is configured to be a web proxy will not allow any ftp, gopher, telnet or other traffic through

## Slide 75: Application Level

## Slide 76: Stateful Multilayer
Stateful multilayer inspection firewalls combine the aspects of the other three types of firewalls
They filter packets at the network layer, determine whether session packets are legitimate and evaluate contents of packets at the application layer

## Slide 77: Stateful Multilayer

## Slide 78: Outline
Introduction
A Frame for Intrusion Detection System
Intrusion Detection Techniques
Ideas for Improving Intrusion Detection

## Slide 79: What is the Intrusion Detection
Intrusions are the activities that violate the security policy of system.
Intrusion Detection is the process used to identify intrusions.

## Slide 80: Intrusion Detection Sytems
What is an IDS?
  Definition
  Characteristics
  Examples of existing IDS
Strengths/weaknesses of IDS

## Slide 81: What is an IDS?
Definition:
  A piece of software
  Monitors a computer system to detect:
    Intrusion: unauthorized attempts to use the system
    Misuse: abuse of existing privileges
  Responds:
    Log activity
    Notify a designated authority
    Take appropriate countermeasures

## Slide 82: Why Use an IDS?
Security is often expensive/cumbersome:
  Cost
  Restrictions on users/functionality
Designers try to offer users “reasonable” levels of security
Security breaches will still occur
Detection allows:
  Finding and fixing the most serious security holes
  Perhaps holding intruders responsible for their actions
  Limiting the amount of damage an attacker can do

## Slide 83: IDS Characteristics
Detection Model
  Misuse detection vs. anomaly detection
Scope
  Host based, multihost based, network based
Operation
  Off-line vs. real-time
Architecture
  Centralized vs. distributed

## Slide 84: IDS Detection Model
Misuse detection - recognize known attacks
  Define a set of attack signatures
  Detect actions that match a signature
  Add new signatures often
  Examples: ARMD, ASIM, Bro, CSM, CyberCop, GRIDS, Stalker, Tripwire
Anomaly detection - recognize atypical behavior
  Define a set of metrics for the system
  Build a statistical model for those metrics during “normal” operation
  Detect when metrics differ significantly from normal
  Examples: AAFID, MIDAS, NADIR, UNICORN
Hybrid
  Examples: CMDS, DIDS, EMERALD, INBOUNDS, NIDES, RealSecure

## Slide 85: IDS Scope
Host based
  Scrutinize data from a single host
  Examples: ARMD, MIDAS, Tripwire
Multihost based
  Analyze data from multiple hosts
  Examples: AAFID, DIDS, CMDS, CSM, NIDES, Stalker
Network based
  Examine network traffic (and possibly data from the connected hosts)
  Examples: ASIM, Bro, CyberCop, EMERALD, GRIDS, INBOUNDS, NADIR, RealSecure, UNICORN

## Slide 86: IDS Architecture
Centralized
  Data collected from single or multiple hosts
  All data shipped to a central location for analysis
  Examples: ARMD, ASIM, Bro, CMDS, CSM, CyberCop, DIDS,
  MIDAS, NADIR, NIDES, RealSecure, Stalker, Tripwire, UNICORN
Hierarchical
  Data collected from multiple hosts
  Data is analyzed as it is passed up through the layers
  Examples: EMERALD, INBOUNDS
Distributed
  Data collected at each host
  Distributed analysis of the data
  Examples: AAFID, CSM, GRIDS

## Slide 87: Types of Intrusion Detection System(1)
Based on the sources of the audit information used by each IDS, the IDSs may be classified into
  Host-base IDSs
  Distributed IDSs
  Network-based IDSs

## Slide 88: Types of Intrusion Detection System(2)
Host-based IDSs
  Get audit data from host audit trails.
  Detect attacks against a single host
Distributed IDSs
  Gather audit data from multiple host and possibly the network that connects the hosts
  Detect attacks involving multiple hosts
Network-Based IDSs
  Use network traffic as the audit data source, relieving the burden on the hosts that usually provide normal computing services
  Detect attacks from network.

## Slide 89: Intrusion Detection Techniques
Misuse detection
  Catch the intrusions in terms of the characteristics of known attacks or system vulnerabilities.
Anomaly detection
  Detect any action that significantly deviates from the normal behavior.

## Slide 90: Misuse Detection
Based on known attack actions.
Feature extract from known intrusions
Integrate the Human knowledge.
The rules are pre-defined
Disadvantage:
  Cannot detect novel or unknown attacks

## Slide 91: Anomaly Detection
Based on the normal behavior of a subject. Sometime assume the training audit data does not include intrusion data.
Any action that significantly deviates from the normal behavior is considered intrusion.

## Slide 92: Anomaly Detection Disadvantages
Based on audit data collected over a period of normal operation.
  When a noise(intrusion) data in the training data, it will make a mis-classification.
How to decide the features to be used. The features are usually decided by domain experts. It may be not completely.

## Slide 93: Misuse Detection vs. Anomaly Detection
 | Advantage | Disadvantage
Misuse Detection | Accurately and generate much fewer false alarm | Cannot detect novel or unknown attacks
Anomaly Detection | Is able to detect unknown attacks based on audit | High false-alarm and limited by training data.

## Slide 94: Intrusion Detection Approaches
Define and extract the features of behavior in system
Define and extract the Rules of Intrusion
Apply the rules to detect the intrusion
Training
Audit Data
Features
Rules
Audit Data
Pattern matching
or Classification
1
3
3
2

## Slide 96: Chapter 1 INTRODUCTION TO WIRELESS COMMUNICATION SYSTEMS

## Slide 97: 1.1 Evolution of Mobile Radio Communications
Major Mobile Radio Systems
  1934 - Police Radio uses conventional AM mobile communication system.
  1935 - Edwin Armstrong demonstrate FM
  1946 - First public mobile telephone service - push-to-talk
  1960 - Improved Mobile Telephone Service, IMTS - full duplex
  1960 - Bell Lab introduce the concept of Cellular mobile system
  1968 - AT&T propose the concept of Cellular mobile system to FCC.
  1976 - Bell Mobile Phone service, poor service due to call blocking
  1983 - Advanced Mobile Phone System (AMPS), FDMA, FM
  1991 - Global System for Mobile (GSM), TDMA, GMSK
  1991 - U.S. Digital Cellular (USDC) IS-54, TDMA, DQPSK
  1993 - IS-95, CDMA, QPSK, BPSK

## Slide 98: 1.2 Example of Mobile Radio Systems
Examples
  Cordless phone
  Remote controller
  Hand-held walkie-talkies
  Pagers
  Cellular telephone
  Wireless LAN
Mobile - any radio terminal that could be moves during operation
Portable - hand-held and used at walking speed
Subscriber - mobile or portable user

## Slide 99
Classification of mobile radio transmission system
  Simplex: communication in only one direction
  Half-duplex: same radio channel for both transmission and reception (push-to-talk)
  Full-duplex: simultaneous radio transmission and reception (FDD, TDD)
Frequency division duplexing uses two radio channel
  Forward channel: base station to mobile user
  Reverse channel: mobile user to base station
Time division duplexing shares a single radio channel in time.

## Slide 101
1.2.2 Paging Systems
Conventional paging system send brief messages to a subscriber
Modern paging system: news headline, stock quotations, faxes, etc.
Simultaneously broadcast paging message from each base station (simulcasting)
Large transmission power to cover wide area.

## Slide 102
1.2.3 Cordless Telephone System
Cordless telephone systems are full duplex communication systems.
First generation cordless phone
  in-home use
  communication to dedicated base unit
  few tens of meters
Second generation cordless phone
  outdoor
  combine with paging system
  few hundred meters per station

## Slide 103
1.2.4 Cellular Telephone Systems
Provide connection to the PSTN for any user location within the radio range of the system.
Characteristic
  Large number of users
  Large Geographic area
  Limited frequency spectrum
  Reuse of the radio frequency by the concept of “cell’’.
Basic cellular system: mobile stations, base stations, and mobile switching center.

## Slide 104
Communication between the base station and mobiles is defined by the standard common air interface (CAI)
  forward voice channel (FVC): voice transmission from base station to mobile
  reverse voice channel (RVC): voice transmission from mobile to base station
  forward control channels (FCC): initiating mobile call from base station to mobile
  reverse control channel (RCC): initiating mobile call from mobile to base station

## Slide 105: Thank you!

## Slide 107
www.studymafia.org
Submitted To: Submitted By:
www.studymafia.org www.studymafia.org
Seminar
On
MOBILE JAMMER

## Slide 108: Content
What is Mobile Jammer?
History.
How Mobile Jammer works?
Jamming Techniques.
Design Parameters/Specification.
Block Diagram.
Power Supply.
Types of Jammer Device.
Application.
Future scope of Jamming Technology.
Conclusion.
Bibliography.
2

## Slide 109: What is Mobile Jammer?
A mobile phone jammer is an instrument used to prevent cellular phones from receiving signals from base stations.
It is a device that transmit signal on the same frequency at which the GSM system operates, the jamming success when the mobile phones in the area where the jammer is located are disabled.
3

## Slide 110: History
Mobile Jammer were originally developed for law enforcement and the military to interrupt communications by criminals and terrorists.
Some were also designed to foil the use of certain remotely detonated explosives.
4

## Slide 111
A jamming device transmits - same radio frequencies of greater power as the cell phone, disrupting the communication between the phone and the cell-phone base station in the tower. It's a called a denial-of-service attack.
How Mobile jammer works

## Slide 112
This causes interference with communication of cell phones and towers to render the phones unusable. On most phones, the network would be out of range.
So Jammers work by either disrupting phone to tower freq.. or tower to phone frequencies.

## Slide 113: Jamming Techniques
Type "A" Device: JAMMERS
Type “B” Device: INTELLIGENT CELLULAR DISABLERS
Type “C” Device: INTELLIGENT BEACON DISABLERS
Type “D” Device: DIRECT RECEIVE & TRANSMIT JAMMERS
Type “E” Device: EMI SHIELD - PASSIVE JAMMING

## Slide 114: Jamming Techniques
1. Type "A" Device: JAMMERS
This type of device comes equipped with several independent oscillators transmitting ’jamming signals’ capable of blocking frequencies used by paging devices as well as those used by cellular systems control channels for call establishment.

## Slide 115: Jamming Techniques
2.Type “B” Device: INTELLIGENT CELLULAR DISABLERS
Unlike jammers, Type ”B” devices do not transmit an interfering signal on the control channels. The device, when located in a designated ’quite’ area, functions as a ’detector’. It has a unique identification number for communicating with the cellular base station.

## Slide 116: Jamming Techniques
3. Type “C” Device (Intelligent Beacon Disablers)
Unlike jammers, Type C devices do not transmit an interfering signal on the control channels. The device, when located in a designated ’quiet’ area, functions as a ’beacon’ and any compatible terminal is instructed to disable its ringer or disable its operation, while within the coverage area of beacon.

## Slide 117: Jamming Techniques
4. Type “D” Device (Direct Receive & Transmit Jammers)
This jammer behaves like a small, independent and portable base station, which can directly interact intelligently or unintelligently with the operation of the local mobile phone. The jammer is predominantly in receive mode and will intelligently choose to interact and block the cell Phone directly if it is within close proximity of the jammer.

## Slide 118: Jamming Techniques
5. Type E Device (EMI Shield - Passive Jamming)
This technique is using EMI suppression techniques to make a room into what is called Faraday cage. Although labor intensive to construct, the Faraday cage essentially Blocks or greatly attenuates, virtually all electromagnetic radiation from entering or leaving the cage - or in this case a target room.

## Slide 119: Design Parameters/Specification
Free space loss {F}= Path Loss (dB)= 32.44 + 20 log D(km) + 20log f(MHz)
The frequency bands
Distance to be jammed (D)
Power calculations

## Slide 120: Block Diagram
If section
Rf section
Jamming signals
Power supply

## Slide 121: Power Supply
Transformer
Rectifier
Regulator
filter

## Slide 122
Contd.
Mobile Jammer

## Slide 123: Types of Jammer Device
Types of cell phone jammer device. There are many types of cell phone jammer device which is used in our daily life .as we take a example of class room, where we does not want to use of cell phone than there we can use cell phone jammer device. By this we can produce the interface between the cell phone base station and cell phone. resulting it disconnect the cell from base station. and we can not receive the any calls from base station.
For this there are many types of cell phone jammer devices which is given as below:
17

## Slide 124
    Remote Control Mobile jammer
    Adjustable Mobile Jammer
    School &Prison Mobile Jammer
    Explosion – Proof Mobile jammer
    Police & Military Mobile Jammer
    Portable Mobile Jammer
18

## Slide 125
19

## Slide 126: Application
To maintain the complete silence in library and lecture hall
To avoid fraud in examination hall
To avoid disturbance in class room
For providing security in business conference, board of directors rooms, seminars, etc.,
For providing calm and peaceful atmosphere in Hospitals
Church/Mosques/Cathedral/Temple/Religious establishment

## Slide 127: Future scope of Jamming Technology
While the law clearly prohibits using a device to actively disrupt a cell-phone signal, there are no rules against passive cell-phone blocking.
Companies are working on devices that control a cell phone but do not "jam the signal.

## Slide 128: Conclusion
Every technology has good aspect as well as bad aspect the important thing is, how we are using it.
Cell phone jammers are very useful to the society from the anti-social elements. We can save our national leaders. we can restrict the communication network between the anti-social elements by using the Mobile jammers. Cell phone jammers prevent the students from carrying cell phones to the colleges.

## Slide 129: Mobile Technologies Challenges and Case Studies
Phuong Nguyen
University of Basel
Switzerland

## Slide 130: Outline
Overview of mobile technologies
Advantages of mobile devices
Challenges
CoMobile, collaborative tasks with mobile phone
Conclusion

## Slide 131: Device for voice communication
Alexander Graham Bell (1876)

## Slide 132: Everyday life‘s tools
Computer
Email
Fax
Radio
Music player
Word processor
Credit cards

## Slide 133: Everyday life‘s tools
Computer
Email
Fax
Radio
Music player
Word processor
Smart phone
Mobile phones are first introduced in mid 1980s
Additional features can be installed

## Slide 134: Mobile applications
Banking (check balance, make transaction)
Restaurant (order and payment)
Mobile Payment (ticket, vending machine)
Tourism: tourist guide
Education: mobile learning
Entertainment: interactive digital art
Scientific: controlling and monitoring

## Slide 135: Interactive Digital Art - TelcomGallery
Use mobile phone to interact with the object:
- Pressing the phone's keys
Speaking to the phone,
Or simply holding the call.
Voice of the user can change the audio-visual
parameters of the digital artworks in real-time

## Slide 136: Mobile devices as remote control

## Slide 137: Advantages of mobile devices
Accessible anywhere, anytime
Conveniently controlling and monitoring
Instant notification
Easy to exchange data and information

## Slide 138: Challenges
Small screen-size (will remains)
Limited input facilities (will remains?)
Diverse software environments:
OS (Symbian, Linux, Windows Mobile), Language (J2ME, BREW, C++)
Limited bandwidth (will be solved):
GSM->GPRS->UMTS, CDMA, WiFi

## Slide 139: Question
How can we use mobile devices efficiently?
(One answer is in next slides)

## Slide 140: Uni Basel-CoMobile overview
Collaboration between: web clients and mobile clients
Diverse communication channels:
SMS, MMS, Voice, WAP, HTTP, Bluetooth
Modularity: flexible and extendable

## Slide 141: Uni Basel-CoMobile architecture

## Slide 142: Example
Jobs done: 40
Queues : 30
Status: OK
Elapsed time: 1 hour
Remain time: 2 hours
Short text can be sent via SMS
Client-side globus-hostname command is not returning a fully qualified domain name (FQN).
The submission scripts use globus-hostname to send information to the server about how to contact the client.
The fix is to make globus-hostname return the FQDN.
There are firewalls and ports (GRAM: 2119, LDAP: 2135) which are not open.
Check that GLOBUS_TCP_PORT_RANGE is set to 3000 to 3090 on the client
(or another range acceptable for the server to contact the client on),
and that all intermediate firewalls are open for this range in both directions.
GRAM Job submission failed because the executable file permissions do not allow execution".
Probable cause: You submitted a script, e.g., globus-job-run symphony:2119/jobmanager-loadleveler $PWD/simple.
ll but simple.ll does not have the execute permission bit set.
The error msg "Authentication Failed remote certificate signed by unknown CA"
means the client cannot find the CA for the cert presented by the server.
Make sure the CA cert is present in the trusted cert dir set with setup-gsi.
Also, check the time is consistent across the machines.
The error msg "GRAM Job submission failed because the connection to the server failed (check host and port)
Make sure that the gatekeeper service is enabled.
The error msg "GRAM Job submission failed because data transfer to the server failed"
means the job manager has problems opening some file.
Make sure $GLOBUS_LOCATION is readable by all the users (mode 755)
What about this text?

## Slide 143: Uni Basel-CoMobile demo
Demo : Text to Speech, and access via phone

## Slide 144: Uni Basel-CoMobile features
Data submission: send information (text, images, audio, video) via SMS, MMS, voice recording.
Receive SMS notification (replies, reminds, alerts).
Access information via various channels: Voice, SMS, MMS, WAP, Bluetooth.
Search on multimedia contents.

## Slide 145: Search with CoMobile
Search on multimedia content
(video, audio, picture):
Using metadata
Automated speech recognition (ASR)
Optical character recognition (OCR)

## Slide 146: Conclusion
Mobile devices are being used in various kinds of applications.
Uni Basel-CoMobile: an useful framework that support collaborative activities with mobile devices.
CoMobile is designed for extension and integration with other systems.

## Slide 147: Discussion
Cost: Users have to pay for SMS, MMS, as well as voice call. „Flat rate“ package will be common in the near future.
Storage: 1 minute video = 1 MB (approximately). There exists 2GB flash card for mobile phone
Bandwidth: 14.4 kbps (GSM), 140 kbps (GPRS), 1920 kbps (UMTS)

## Slide 148: SMS gateway - Kannel
RS-232
AT Commands
AT+CNMI=1,2,0,1,1
SMS Text
HTTP request to forward SMS Text

## Slide 149: MMS gateway - Mbuni
RS-232
AT Commands
AT+CNMI=1,2,0,1,1
MMS
Text, Picture, Audio
HTTP request to forward MMS
Mbuni

## Slide 150: PBX Asterisk
PCI socket
Voice
AGI: Perl, Java, PHP scripts are called
Telephone line

## Slide 151: Uni Basel-CoMobile-Demo