## Slide 1
WIRELESS NETWORKS
Mrs. M. Lalli
Assistant Professor
Department of Computer Science
Bharathidasan University
Trichy

## Slide 2: Mobile Communication Technology according to IEEE
Local wireless networks
WLAN 802.11
802.11a
802.11b
802.11i/e/…/w
802.11g
WiFi
802.11h
Personal wireless nw
WPAN 802.15
802.15.4
802.15.1
802.15.2
Bluetooth
802.15.4a/b
ZigBee
802.15.3
Wireless distribution networks
WMAN 802.16 (Broadband Wireless Access)
802.20 (Mobile Broadband Wireless Access)
+ Mobility
WiMAX
802.15.3a/b
802.15.5

## Slide 3: Characteristics of wireless LANs
Advantages
  very flexible within the reception area
  Ad-hoc networks without previous planning possible
  (almost) no wiring difficulties (e.g. historic buildings, firewalls)
  more robust against disasters like, e.g., earthquakes, fire - or users pulling a plug...
Disadvantages
  typically very low bandwidth compared to wired networks (1-10 Mbit/s) due to shared medium
  many proprietary solutions, especially for higher bit-rates, standards take their time (e.g. IEEE 802.11)
  products have to follow many national restrictions if working wireless, it takes a vary long time to establish global solutions like, e.g., IMT-2000

## Slide 4: Design goals for wireless LANs
  global, seamless operation
  low power for battery use
  no special permissions or licenses needed to use the LAN
  robust transmission technology
  simplified spontaneous cooperation at meetings
  easy to use for everyone, simple management
  protection of investment in wired networks
  security (no one should be able to read my data), privacy (no one should be able to collect user profiles), safety (low radiation)
  transparency concerning applications and higher layer protocols, but also location awareness if necessary

## Slide 5: Comparison: infrared vs. radio transmission
Infrared
  uses IR diodes, diffuse light, multiple reflections (walls, furniture etc.)
Advantages
  simple, cheap, available in many mobile devices
  no licenses needed
  simple shielding possible
Disadvantages
  interference by sunlight, heat sources etc.
  many things shield or absorb IR light
  low bandwidth
Example
  IrDA (Infrared Data Association) interface available everywhere
Radio
  typically using the license free ISM band at 2.4 GHz
Advantages
  experience from wireless WAN and mobile phones can be used
  coverage of larger areas possible (radio can penetrate walls, furniture etc.)
Disadvantages
  very limited license free frequency bands
  shielding more difficult, interference with other electrical devices
Example
  Many different products

## Slide 6: Comparison: infrastructure vs. ad-hoc networks
infrastructure network
ad-hoc network
AP
AP
AP
wired network
AP: Access Point

## Slide 7: 802.11 - Architecture of an infrastructure network
Station (STA)
  terminal with access mechanisms to the wireless medium and radio contact to the access point
Basic Service Set (BSS)
  group of stations using the same radio frequency
Access Point
  station integrated into the wireless LAN and the distribution system
Portal
  bridge to other (wired) networks
Distribution System
  interconnection network to form one logical network (EES: Extended Service Set) based on several BSS
Distribution System
Portal
802.x LAN
Access
Point
802.11 LAN
BSS2
802.11 LAN
BSS1
Access
Point
STA1
STA2
STA3
ESS
Notes: 9

## Slide 8: 802.11 - Architecture of an ad-hoc network
Direct communication within a limited range
  Station (STA): terminal with access mechanisms to the wireless medium
  Independent Basic Service Set (IBSS): group of stations using the same radio frequency
802.11 LAN
IBSS2
802.11 LAN
IBSS1
STA1
STA4
STA5
STA2
STA3

## Slide 9: ETSI – HIPERLAN (historical)
ETSI standard
  European standard, cf. GSM, DECT, ...
  Enhancement of local Networks and interworking with fixed networks
  integration of time-sensitive services from the early beginning
HIPERLAN family
  one standard cannot satisfy all requirements
    range, bandwidth, QoS support
    commercial constraints
  HIPERLAN 1 standardized since 1996 – no products!
physical layer
channel access
control layer
medium access
control layer
physical layer
data link layer
HIPERLAN layers
OSI layers
network layer
higher layers
physical layer
medium access
control layer
logical link
control layer
IEEE 802.x layers

## Slide 10: Overview: original HIPERLAN protocol family
HIPERLAN 1 never reached product status,
the other standards have been renamed/modfied !

## Slide 11: HIPERLAN 1 - Characteristics
Data transmission
  point-to-point, point-to-multipoint, connectionless
  23.5 Mbit/s, 1 W power, 2383 byte max. packet size
Services
  asynchronous and time-bounded services with hierarchical priorities
  compatible with ISO MAC
Topology
  infrastructure or ad-hoc networks
  transmission range can be larger then coverage of a single node („forwarding“ integrated in mobile terminals)
Further mechanisms
  power saving, encryption, checksums

## Slide 12: HIPERLAN 1 - Physical layer
Scope
  modulation, demodulation, bit and frame synchronization
  forward error correction mechanisms
  measurements of signal strength
  channel sensing
Channels
  3 mandatory and 2 optional channels (with their carrier frequencies)
  mandatory
    channel 0: 5.1764680 GHz
    channel 1: 5.1999974 GHz
    channel 2: 5.2235268 GHz
  optional
    channel 3: 5.2470562 GHz
    channel 4: 5.2705856 GHz

## Slide 13: HIPERLAN 1 - Physical layer frames
Maintaining a high data-rate (23.5 Mbit/s) is power consuming - problematic for mobile terminals
  packet header with low bit-rate comprising receiver information
  only receiver(s) address by a packet continue receiving
Frame structure
  LBR (Low Bit-Rate) header with 1.4 Mbit/s
  450 bit synchronization
  minimum 1, maximum 47 frames with 496 bit each
  for higher velocities of the mobile terminal (> 1.4 m/s) the maximum number of frames has to be reduced
Modulation
  GMSK for high bit-rate, FSK for LBR header
LBR
synchronization
data0
data1
datam-1
. . .
HBR

## Slide 14: HIPERLAN 1 - CAC sublayer
Channel Access Control (CAC)
  assure that terminal does not access forbidden channels
  priority scheme, access with EY-NPMA
Priorities
  5 priority levels for QoS support
  QoS is mapped onto a priority level with the help of the packet lifetime (set by an application)
    if packet lifetime = 0 it makes no sense to forward the packet to the receiver any longer
    standard start value 500ms, maximum 16000ms
    if a terminal cannot send the packet due to its current priority, waiting time is permanently subtracted from lifetime
    based on packet lifetime, waiting time in a sender and number of hops to the receiver, the packet is assigned to one out of five priorities
    the priority of waiting packets, therefore, rises automatically

## Slide 15: HIPERLAN 1 - EY-NPMA I
prioritization
EY-NPMA (Elimination Yield Non-preemptive Priority Multiple Access)
  3 phases: priority resolution, contention resolution, transmission
  finding the highest priority
    every priority corresponds to a time-slot to send in the first phase, the higher the priority the earlier the time-slot to send
    higher priorities can not be preempted
    if an earlier time-slot for a higher priority remains empty, stations with the next lower priority might send
    after this first phase the highest current priority has been determined
contention
transmission
transmission
synchronization
priority detection
priority assertion
t
user data
elimination burst
elimination survival
verification
yield listening
IYS
IPS
IPA
IES
IESV

## Slide 16: HIPERLAN 1 - EY-NPMA II
Several terminals can now have the same priority and wish to send
  contention phase
    Elimination Burst: all remaining terminals send a burst to eliminate contenders (11111010100010011100000110010110, high bit- rate)
    Elimination Survival Verification: contenders now sense the channel, if the channel is free they can continue, otherwise they have been eliminated
    Yield Listening: contenders again listen in slots with a nonzero probability, if the terminal senses its slot idle it is free to transmit at the end of the contention phase
    the important part is now to set the parameters for burst duration and channel sensing (slot-based, exponentially distributed)
  data transmission
    the winner can now send its data (however, a small chance of collision remains)
    if the channel was idle for a longer time (min. for a duration of 1700 bit) a terminal can send at once without using EY-NPMA
  synchronization using the last data transmission

## Slide 17: HIPERLAN 1 - DT-HCPDU/AK-HCPDU
1
0
1
0
1
0
1
0
0
1
HI
HDA
HDA
HDACS
BLIR = n
1
BL-
IRCS
LBR
0
1
2
3
4
5
6
7
bit
HBR
0
1
2
3
4
5
6
7
bit
TI
BLI = n
byte
1
PLI = m
HID
2
3 - 6
DA
7 - 12
SA
13 - 18
UD
19 - (52n-m-4)
PAD
(52n-m-3) - (52n-4)
CS
(52n-3) - 52n
1
0
1
0
1
0
1
0
0
1
HI
AID
AID
AIDCS
LBR
0
1
2
3
4
5
6
7
bit
Data HCPDU
Acknowledgement HCPDU
HI: HBR-part Indicator
HDA: Hashed Destination HCSAP Address
HDACS: HDA CheckSum
BLIR: Block Length Indicator
BLIRCS: BLIR CheckSum
TI: Type Indicator
BLI: Block Length Indicator
HID: HIPERLAN IDentifier
DA: Destination Address
SA: Source Address
UD: User Data (1-2422 byte)
PAD: PADding
CS: CheckSum
AID: Acknowledgement IDentifier
AIDS: AID CheckSum

## Slide 18: HIPERLAN 1 - MAC layer
Compatible to ISO MAC
Supports time-bounded services via a priority scheme
Packet forwarding
  support of directed (point-to-point) forwarding and broadcast forwarding (if no path information is available)
  support of QoS while forwarding
Encryption mechanisms
  mechanisms integrated, but without key management
Power conservation mechanisms
  mobile terminals can agree upon awake patterns (e.g., periodic wake-ups to receive data)
  additionally, some nodes in the networks must be able to buffer data for sleeping terminals and to forward them at the right time (so called stores)

## Slide 19: HIPERLAN 1 - DT-HMPDU
LI: Length Indicator
TI: Type Indicator
RL: Residual Lifetime
PSN: Sequence Number
DA: Destination Address
SA: Source Address
ADA: Alias Destination Address ASA: Alias Source Address
UP: User Priority
ML: MSDU Lifetime
KID: Key Identifier
IV: Initialization Vector
UD: User Data, 1–2383 byte
SC: Sanity Check (for the unencrypted PDU)
n= 40–2422
0
1
2
3
4
5
6
7
bit
LI = n
byte
1 - 2
TI = 1
RL
3
4 - 5
PSN
6 - 7
DA
8 - 13
SA
14 - 19
ADA
20 - 25
ASA
26 - 31
UP
ML
ML
KID
IV
IV
UD
SC
32
33
34
35 - 37
38 - (n-2)
(n-1) - n
Data HMPDU

## Slide 20: Information bases
Route Information Base (RIB) - how to reach a destination
  [destination, next hop, distance]
Neighbor Information Base (NIB) - status of direct neighbors
  [neighbor, status]
Hello Information Base (HIB) - status of destination (via next hop)
  [destination, status, next hop]
Alias Information Base (AIB) - address of nodes outside the net
  [original MSAP address, alias MSAP address]
Source Multipoint Relay Information Base (SMRIB) - current MP status
  [local multipoint forwarder, multipoint relay set]
Topology Information Base (TIB) - current HIPERLAN topology
  [destination, forwarder, sequence]
Duplicate Detection Information Base (DDIB) - remove duplicates
  [source, sequence]

## Slide 21: Ad-hoc networks using HIPERLAN 1
neighborhood
(i.e., within radio range)
Information Bases (IB):
RIB: Route
NIB: Neighbor
HIB: Hello
AIB: Alias
SMRIB: Source Multipoint Relay
TIB: Topology
DDIB: Duplicate Detection
RIB
NIB
HIB
AIB
SMRIB
TIB
DDIB
RIB
NIB
HIB
AIB
SMRIB
TIB
DDIB
RIB
NIB
HIB
AIB
SMRIB
TIB
DDIB
RIB
NIB
HIB
AIB
DDIB
RIB
NIB
HIB
AIB
DDIB
RIB
NIB
HIB
AIB
DDIB
1
2
3
4
5
6
Forwarder
Forwarder
Forwarder

## Slide 22: Some history: Why wireless ATM?
seamless connection to wired ATM, a integrated services high-performance network supporting different types a traffic streams
ATM networks scale well: private and corporate LANs, WAN
B-ISDN uses ATM as backbone infrastructure and integrates several different services in one universal system
mobile phones and mobile communications have an ever increasing importance in everyday life
current wireless LANs do not offer adequate support for multimedia data streams
merging mobile communication and ATM leads to wireless ATM from a telecommunication provider point of view
goal: seamless integration of mobility into B-ISDN
Problem: very high complexity of the system – never reached products

## Slide 23: ATM - basic principle
  favored by the telecommunication industry for advanced high-performance networks, e.g., B-ISDN, as transport mechanism
  statistical (asynchronous, on demand) TDM (ATDM, STDM)
  cell header determines the connection the user data belongs to
  mixing of different cell-rates is possible
    different bit-rates, constant or variable, feasible
  interesting for data sources with varying bit-rate:
    e.g., guaranteed minimum bit-rate
    additionally bursty traffic if allowed by the network
ATM cell:
5 48 [byte]
connection identifier, checksum etc.
cell header
user data

## Slide 24: Cell-based transmission
  asynchronous, cell-based transmission as basis for ATM
  continuous cell-stream
  additional cells necessary for operation and maintenance of the network (OAM cells; Operation and Maintenance)
  OAM cells can be inserted after fixed intervals to create a logical frame structure
  if a station has no data to send it automatically inserts idle cells that can be discarded at every intermediate system without further notice
  if no synchronous frame is available for the transport of cells (e.g., SDH or Sonet) cell boundaries have to be detected separately (e.g., via the checksum in the cell header)

## Slide 25: B-ISDN protocol reference model
physical layer
ATM layer
ATM adaptation layer
higher
layers
higher
layers
control
plane
layer management
plane management
user
plane
planes
layers
3 dimensional reference model
  three vertical planes (columns)
    user plane
    control plane
    management plane
  three hierarchical layers
    physical layer
    ATM layer
    ATM adaptation layer
Out-of-Band-Signaling: user data is transmitted separately from control information
management plane

## Slide 26: ATM layers
Physical layer, consisting of two sub-layers
  physical medium dependent sub-layer
    coding
    bit timing
    transmission
  transmission convergence sub-layer
    HEC (Header Error Correction) sequence generation and verification
    transmission frame adaptation, generation, and recovery
    cell delineation, cell rate decoupling
ATM layer
  cell multiplexing/demultiplexing
  VPI/VCI translation
  cell header generation and verification
  GFC (Generic Flow Control)
ATM adaptation layer (AAL)

## Slide 27: ATM adaptation layer (AAL)
Provides different service classes on top of ATM based on:
  bit rate:
    constant bit rate: e.g. traditional telephone line
    variable bit rate: e.g. data communication, compressed video
  time constraints between sender and receiver:
    with time constraints: e.g. real-time applications, interactive voice and video
    without time constraints: e.g. mail, file transfer
  mode of connection:
    connection oriented or connectionless
AAL consists of two sub-layers:
  Convergence Sublayer (CS): service dependent adaptation
    Common Part Convergence Sublayer (CPCS)
    Service Specific Convergence Sublayer (SSCS)
  Segmentation and Reassembly Sublayer (SAR)
  sub-layers can be empty

## Slide 28: ATM and AAL connections
  ATM layer:
    service independent transport of ATM cells
    multiplex and demultiplex functionality
  AAL layer: support of different services
physical
layer
ATM
AAL
physical
layer
ATM
AAL
end-system A
end-system B
ATM network
service dependent
AAL connections
service independent
ATM connections
application

## Slide 29: Wireless ATM Working Group
Task: development of specifications to enable the use of ATM technology also for wireless networks with a large coverage of current network scenarios (private and public, local and global)
compatibility to existing ATM Forum standards important
it should be possible to easily upgrade existing ATM networks with mobility functions and radio access
two sub-groups of work items
Mobile ATM Protocol Extensions
  handover signaling
  location management
  mobile routing
  traffic and QoS Control
  network management
Radio Access Layer (RAL) Protocols
  radio access layer
  wireless media access control
  wireless data link control
  radio resource control
  handover issues

## Slide 30: WATM services
Office environment
  multimedia conferencing, online multimedia database access
Universities, schools, training centers
  distance learning, teaching
Industry
  database connection, surveillance, real-time factory management
Hospitals
  reliable, high-bandwidth network, medical images, remote monitoring
Home
  high-bandwidth interconnect of devices (TV, CD, PC, ...)
Networked vehicles
  trucks, aircraft etc. interconnect, platooning, intelligent roads

## Slide 31: WATM components
WMT (Wireless Mobile ATM Terminal)
RAS (Radio Access System)
EMAS-E (End-user Mobility-supporting ATM Switch - Edge)
EMAS-N (End-user Mobility-supporting ATM Switch - Network)
M-NNI (Network-to-Network Interface with Mobility support)
LS (Location Server)
AUS (Authentication Server)

## Slide 32: Reference model
WMT
WMT
EMAS-E
EMAS-N
EMAS-N
M-NNI
RAS
RAS
LS
AUS

## Slide 33: User plane protocol layers
WATM
terminal
adapter
MATM
termi-
nal
RAS
EMAS
-E
EMAS
-N
ATM-
Switch
fixed
end
system
radio segment
fixed network segment
RAL
ATM
PHY
PHY
ATM
PHY
AAL
user
process
ATM
AAL
user process
ATM-
CL
ATM
RAL
PHY
ATM-
CL
ATM
PHY
PHY
ATM
PHY
PHY

## Slide 34: Control plane protocol layers
ATM
PHY
SAAL
SIG,
UNI
RAL
M-ATM
SAAL
SIG,
M-UNI
ATM-
CL
ATM
RAL
PHY
ATM-
CL
ATM
PHY
PHY
SAAL
SIG,
M-UNI,
M-PNNI
ATM
PHY
PHY
SAAL
SIG,
M-PNNI
ATM
PHY
PHY
SAAL
SIG,
PNNI,
UNI
WATM
terminal
adapter
MATM
termi-
nal
RAS
EMAS
-E
EMAS
-N
ATM-
Switch
fixed
end
system
radio segment
fixed network segment

## Slide 35: Reference model with further access scenarios I
1: wireless ad-hoc ATM network
2: wireless mobile ATM terminals
3: mobile ATM terminals
4: mobile ATM switches
5: fixed ATM terminals
6: fixed wireless ATM terminals
WMT: wireless mobile terminal
WT: wireless terminal
MT: mobile terminal
T: terminal
AP: access point
EMAS: end-user mobility supporting ATM switch (-E: edge, -N: network)
NMAS: network mobility supporting ATM switch
MS: mobile ATM switch

## Slide 36: Reference model with further access scenarios II
RAS
ACT
WMT
WMT
NMAS
RAS
RAS
MS
T
EMAS
-E
MT
WT
RAS
EMAS
-N
T
RAS
EMAS
-E
WMT
1
2
3
4
5
6

## Slide 37: HAND OVER
Handover of multiple connections
Handover of point-to-multipoint connections
QOS support
Data integrity and security
Signaling and routing support
Performance and complexity

## Slide 38: Location Management
Transparency of mobility
Security
Efficiency and scalability
Identification
Inter-working and standards

## Slide 39: Mobile QOS
Wired QOS
Wireless QOS
Handover QOS
- Hard Handover QOS
- Soft Handover QOS

## Slide 40: Bluetooth
Idea
  Universal radio interface for ad-hoc wireless connectivity
  Interconnecting computer and peripherals, handheld devices, PDAs, cell phones – replacement of IrDA
  Embedded in other devices, goal: 5€/device (2005: 40€/USB bluetooth)
  Short range (10 m), low power consumption, license-free 2.45 GHz ISM
  Voice and data transmission, approx. 1 Mbit/s gross data rate
One of the first modules (Ericsson).

## Slide 41: Bluetooth
History
  1994: Ericsson (Mattison/Haartsen), “MC-link” project
  Renaming of the project: Bluetooth according to Harald “Blåtand” Gormsen [son of Gorm], King of Denmark in the 10th century
  1998: foundation of Bluetooth SIG, www.bluetooth.org
  1999: erection of a rune stone at Ercisson/Lund ;-)
  2001: first consumer products for mass market, spec. version 1.1 released
  2005: 5 million chips/week
Special Interest Group
  Original founding members: Ericsson, Intel, IBM, Nokia, Toshiba
  Added promoters: 3Com, Agere (was: Lucent), Microsoft, Motorola
  > 2500 members
  Common specification and certification of products
(was: )

## Slide 42: History and hi-tech…
1999:
Ericsson mobile communications AB reste denna sten till minne av Harald Blåtand, som fick ge sitt namn åt en ny teknologi för trådlös, mobil kommunikation.

## Slide 43: Characteristics
2.4 GHz ISM band, 79 (23) RF channels, 1 MHz carrier spacing
  Channel 0: 2402 MHz … channel 78: 2480 MHz
  G-FSK modulation, 1-100 mW transmit power
FHSS and TDD
  Frequency hopping with 1600 hops/s
  Hopping sequence in a pseudo random fashion, determined by a master
  Time division duplex for send/receive separation
Voice link – SCO (Synchronous Connection Oriented)
  FEC (forward error correction), no retransmission, 64 kbit/s duplex, point-to-point, circuit switched
Data link – ACL (Asynchronous ConnectionLess)
  Asynchronous, fast acknowledge, point-to-multipoint, up to 433.9 kbit/s symmetric or 723.2/57.6 kbit/s asymmetric, packet switched
Topology
  Overlapping piconets (stars) forming a scatternet

## Slide 44: Piconet
Collection of devices connected in an ad hoc fashion
One unit acts as master and the others as slaves for the lifetime of the piconet
Master determines hopping pattern, slaves have to synchronize
Each piconet has a unique hopping pattern
Participation in a piconet = synchronization to hopping sequence
Each piconet has one master and up to 7 simultaneous slaves (> 200 could be parked)
M=Master
S=Slave
P=Parked
SB=Standby
M
S
P
SB
S
S
P
P
SB

## Slide 45: Forming a piconet
All devices in a piconet hop together
  Master gives slaves its clock and device ID
    Hopping pattern: determined by device ID (48 bit, unique worldwide)
    Phase in hopping pattern determined by clock
Addressing
  Active Member Address (AMA, 3 bit)
  Parked Member Address (PMA, 8 bit)
SB
SB
SB
SB
SB
SB
SB
SB
SB
M
S
P
SB
S
S
P
P
SB



















## Slide 46: Scatternet
Linking of multiple co-located piconets through the sharing of common master or slave devices
  Devices can be slave in one piconet and master of another
Communication between piconets
  Devices jumping back and forth between the piconets
M=Master
S=Slave
P=Parked
SB=Standby
M
S
P
SB
S
S
P
P
SB
M
S
S
P
SB
Piconets
(each with a
capacity of
720 kbit/s)

## Slide 47: Bluetooth protocol stack
Radio ( specify air interface)
Baseband ( conn establish, packet format, timing, Qos parameters)
Link Manager
Control
Host
Controller
Interface
Logical Link Control and Adaptation Protocol (L2CAP)
Audio
TCS BIN
SDP
OBEX
vCal/vCard
IP
NW apps.
TCP/UDP
BNEP
RFCOMM (serial line interface)
AT modem
commands
telephony apps.
audio apps.
mgmnt. apps.
AT: attention sequence
OBEX: object exchange
TCS BIN: telephony control protocol specification – binary- Call ctrl for bluetooth devices
BNEP: Bluetooth network encapsulation protocol
SDP: service discovery protocol
RFCOMM: radio frequency comm.
PPP

## Slide 48: Frequency selection during data transmission
S
fk
625 µs
fk+1
fk+2
fk+3
fk+4
fk+3
fk+4
fk
fk
fk+5
fk+5
fk+1
fk+6
fk+6
fk+6
M
M
M
M
M
M
M
M
M
t
t
t
S
S
S
S
S

## Slide 49: Baseband- packet format
Piconet/channel definition
Low-level packet definition
  Access code
    Channel, device access, e.g., derived from master
  Packet header
    1/3-FEC, active member address (broadcast +7 slaves), link type, alternating bit ARQ/SEQ, checksum
access code
packet header
payload
68(72)
54
0-2745
bits
AM address
type
flow
ARQN
SEQN
HEC
3
4
1
1
1
8
bits
preamble
sync.
(trailer)
4
64
(4)

## Slide 50: SCO (synchronous connection oriented link )payload types
payload (30)
audio (30)
audio (10)
audio (10)
HV3
HV2
HV1
DV
FEC (20)
audio (20)
FEC (10)
header (1)
payload (0-9)
2/3 FEC
CRC (2)
(bytes)

## Slide 51: ACL(Asynchronous connectionless link) Payload types
payload (0-343)
header (1/2)
payload (0-339)
CRC (2)
header (1)
payload (0-17)
2/3 FEC
header (1)
payload (0-27)
header (2)
payload (0-121)
2/3 FEC
header (2)
payload (0-183)
header (2)
payload (0-224)
2/3 FEC
header (2)
payload (0-339)
DH5
DM5
DH3
DM3
DH1
DM1
header (1)
payload (0-29)
AUX1
CRC (2)
CRC (2)
CRC (2)
CRC (2)
CRC (2)
CRC (2)
(bytes)

## Slide 52: Baseband data rates
Payload User Symmetric Asymmetric
Header Payload max. Rate max. Rate [kbit/s]
Type [byte] [byte] FEC CRC [kbit/s] Forward Reverse
DM1 1 0-17 2/3 yes 108.8 108.8 108.8
DH1 1 0-27 no yes 172.8 172.8 172.8
DM3 2 0-121 2/3 yes 258.1 387.2 54.4
DH3 2 0-183 no yes 390.4 585.6 86.4
DM5 2 0-224 2/3 yes 286.7 477.8 36.3
DH5 2 0-339 no yes 433.9 723.2 57.6
AUX1 1 0-29 no no 185.6 185.6 185.6
HV1 na 10 1/3 no 64.0
HV2 na 20 2/3 no 64.0
HV3 na 30 no no 64.0
DV 1 D 10+(0-9) D 2/3 D yes D 64.0+57.6 D
ACL
1 slot
3 slot
5 slot
SCO
Data Medium/High rate, High-quality Voice, Data and Voice

## Slide 53: Baseband link types
Polling-based TDD packet transmission
  625µs slots, master polls slaves
SCO (Synchronous Connection Oriented) – Voice
  Periodic single slot packet assignment, 64 kbit/s full-duplex, point-to-point
ACL (Asynchronous ConnectionLess) – Data
  Variable packet size (1,3,5 slots), asymmetric bandwidth, point-to-multipoint
MASTER
SLAVE 1
SLAVE 2
f6
f0
f1
f7
f12
f13
f19
f18
SCO
SCO
SCO
SCO
ACL
f5
f21
f4
f20
ACL
ACL
f8
f9
f17
f14
ACL

## Slide 54: Robustness
Slow frequency hopping with hopping patterns determined by a master
  Protection from interference on certain frequencies
  Separation from other piconets (FH-CDMA)
Retransmission
  ACL only, very fast
Forward Error Correction
  SCO and ACL
MASTER
SLAVE 1
SLAVE 2
A
C
C
H
F
G
G
B
D
E
NAK
ACK
Error in payload
(not header!)

## Slide 55: L2CAP - Logical Link Control and Adaptation Protocol
Simple data link protocol on top of baseband
Connection oriented, connectionless, and signalling channels
Protocol multiplexing
  RFCOMM, SDP, telephony control
Segmentation & reassembly
  Up to 64kbyte user data, 16 bit CRC used from baseband
QoS flow specification per channel
  Follows RFC 1363, specifies delay, jitter, bursts, bandwidth
Group abstraction
  Create/close group, add/remove member

## Slide 56: L2CAP logical channels
baseband
L2CAP
baseband
L2CAP
baseband
L2CAP
Slave
Slave
Master
ACL
2
d
1
d
d
1
1
d
2
1
signalling
connectionless
connection-oriented
d
d
d

## Slide 57: Additional protocols to support legacy protocols/apps.
RFCOMM
  Emulation of a serial port (supports a large base of legacy applications)
  Allows multiple ports over a single physical channel
Telephony Control Protocol Specification (TCS)
  Call control (setup, release)
  Group management
OBEX
  Exchange of objects, IrDA replacement
WAP
  Interacting with applications on cellular phones

## Slide 58: Profiles
Represent default solutions for a certain usage model
  Vertical slice through the protocol stack
  Basis for interoperability
Generic Access Profile
Service Discovery Application Profile
Cordless Telephony Profile
Intercom Profile
Serial Port Profile
Headset Profile
Dial-up Networking Profile
Fax Profile
LAN Access Profile
Generic Object Exchange Profile
Object Push Profile
File Transfer Profile
Synchronization Profile
Additional Profiles
Advanced Audio Distribution
PAN
Audio Video Remote Control
Basic Printing
Basic Imaging
Extended Service Discovery
Generic Audio Video Distribution
Hands Free
Hardcopy Cable Replacement
Profiles
Protocols
Applications

## Slide 59: Thank you!!!!!!!!!