## Slide 1
COMPUTER ORGANIZATION
ARCHITECTURE
Dr.B.Smitha

## Slide 2: CPU
Arithmetic and Logic Unit (ALU)
It performs all the arithmetic and logical micro operations.
Floating Point Unit (FPU)
It performs operations on floating point numbers.
Memory Unit (MU)
It stores the set of instructions.
Control Unit (CU)
It supervises the sequence of micro operations.
Registers
Temporary storage area, which holds the data during the execution of an instruction.
CU
FPU
MU
REGISTERS
ALU

## Slide 3: Registers inside CPU
A (8-bit)
B (8-bit)
C (8-bit)
D (8-bit)
E (8-bit)
H (8-bit)
L (8-bit)
PC (16-bit)
SP (16-bit)
S | Z |  | A C |  | P |  | C Y
General Purpose Registers
Index Registers
Accumulator
Flag Register / Program Status Word (PSW)
S = Sign, Z = Zero, CY = Carry, AC = Auxiliary Carry, P = Parity,

## Slide 4
Microprocessor executes the instructions stored in memory (RAM).
It executes one instruction at a time.
Each of the instruction contains operations and operands.
Operation specifies the type of action to be performed.
  For example: ADD, SUB, MOV, INC, LOAD, STORE
Operands are the data on which the operation is to be performed.
Here MOV is operation and (B & A) are operands.
MOV B, A
ADD B
Here ADD is operation and (B) is operand.

## Slide 5
Operand can be place either in one of the processor register or in
memory.
There are different ways to get the operands.
The way in which the operand is taken from register or memory is named as addressing mode.

## Slide 6
Immediate Addressing Mode
Register Addressing Mode
Register Indirect Addressing Mode
Direct Addressing Mode
Indirect Addressing Mode
Implied Addressing Mode
Relative Addressing Mode
Indexed Addressing Mode
Base Register Addressing Mode
Autoincrement or Autodecrement Addressing Mode
Types of Addressing Modes

## Slide 7: 1. Immediate Addressing Mode
The operand is specified with in the instruction.
Operand itself is provided in the instruction rather than its address.
Move Immediate
MVI A , 15h A ← 15h
Here 15h is the immediate operand
Add Immediate
ADI 3Eh
A ← A + 3Eh
Here 3Eh is the immediate operand

## Slide 8: 2. Register Addressing Mode
The operand is specified with in one of the processor register.
Instruction specifies the register in which the operand is stored.
MOV C , A
Move
C ← A Here A is the operand specified in register
ADD B
A ← A + B
Add
Here B is the operand specified in register

## Slide 9: 3. Register Indirect Addressing Mode
The instruction specifies the register in which the memory address of operand is placed.
It do not specify the operand itself but its location with in the memory where operand is placed.
MOV A , M
Move
A ← [[H][L]]
It moves the data from memory location specified by HL register pair to A.

## Slide 10: 3. Register Indirect Addressing Mode
2807 | 
2806 | 
2805 | A9
2804 | 
2803 | 
2802 | 
2801 | 
2800 | 
H | 28
L | 05
2807 | 
2806 | 
2805 | A9
2804 | 
2803 | 
2802 | 
2801 | 
2800 | 
A | A9
H | 28
L | 05
MOV A , M A ← [[H][L]]
It moves the data from memory location specified by HL register pair to A
Before After
A
A ← [2805]
A ← A9

## Slide 11: 4. Direct Addressing Mode
The instruction specifies the direct address of the operand.
The memory address is specified where the actual operand is.
Load Accumulator
LDA 2805h A ← [2805]
It loads the data from memory location 2805 to A.
Store Accumulator
STA 2803h [2803] ← A
It stores the data from A to memory location 2803.

## Slide 12: 4. Direct Addressing Mode
2807 | 
2806 | 
2805 | 5C
2804 | 
2803 | 
2802 | 
2801 | 
2800 | 
A
2807 | 
2806 | 
2805 | 5C
2804 | 
2803 | 
2802 | 
2801 | 
2800 | 
A | 5C
LDA 2805h A ← [2805]
It loads the data from memory location 2805 to A.
Before After
A ← [2805]
A ← 5C

## Slide 13: 4. Direct Addressing Mode
2807
2806
2805
2804
2803
2802
2801
2800
A | 9B
2807 | 
2806 | 
2805 | 
2804 | 
2803 | 9B
2802 | 
2801 | 
2800 | 
A | 9B
STA 2803h [2803] ← A
It stores the data from A to memory location 2803.
Before After
[2803] ← A
[2803] ← 9B

## Slide 14: 5. Indirect Addressing Mode
The instruction specifies the indirect address where the effective address of the operand is placed.
The memory address is specified where the actual address of operand is placed.
Move
MOV A, 2802h A ← [[2802]]
It moves the data from memory location specified by the location 2802 to A.

## Slide 15: 5. Indirect Addressing Mode
2807 | 
2806 | FF
2805 | 
2804 | 
2803 | 06
2802 | 28
2801 | 
2800 | 
A
2807 | 
2806 | FF
2805 | 
2804 | 
2803 | 06
2802 | 28
2801 | 
2800 | 
A | FF
MOV A, 2802h A ← [[2802]]
It moves the data from memory location specified by the location 2802 to A.
Before After
A ← [[2802]]
A ← FF

## Slide 16: 6. Implied Addressing Mode
It is also called inherent addressing mode.
The operand is implied by the instruction.
The operand is hidden/fixed inside the instruction.
Complement Accumulator CMA
(Here accumulator A is implied by the instruction)
Complement Carry Flag CMC
(Here Flags register is implied by the instruction)
Set Carry Flag STC
(Here Flags register is implied by the instruction)

## Slide 17: 7. Relative Addressing Mode
In relative addressing mode, contents of Program Counter PC is added to address part of instruction to obtain effective address.
The address part of the instruction is called as offset and it can +ve or –ve.
When the offset is added to the PC the resultant number is the memory location where the operand will be placed.

## Slide 18: 7. Relative Addressing Mode
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
PC | 2801
Offset = 04h
Effective address of operand = PC + 01 + offset Effective address of operand = 2801 + 01 + 04 Effective address of operand = 2806h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
Actual Operand

## Slide 19: 7. Relative Addressing Mode
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
PC | 2803
Offset = 03h
Effective address of operand = PC + 01 + offset Effective address of operand = 2803 + 01 + 03 Effective address of operand = 2807h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
Actual Operand

## Slide 20: 8. Indexed Addressing Mode
In index addressing mode, contents of Index register is added to address part of instruction to obtain effective address.
The address part of instruction holds the beginning/base address and is called as base.
The index register hold the index value, which is +ve.
Base remains same, the index changes.
When the base is added to the index register the resultant number is the memory location where the operand will be placed.

## Slide 21: 8. Indexed Addressing Mode
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
IX | 0000
Base = 2800h
Effective address of operand = Base + IX
2800h + 0000h = 2800h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
IX | 0001
2800h + 0001h = 2801h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
IX | 0002
2800h + 0002h = 2802h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
IX | 0003
2800h + 0003h = 2803h

## Slide 22: 8. Indexed Addressing Mode
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
IX | 0000
Base = 2802h
Effective address of operand = Base + IX
2802h + 0000h = 2802h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
IX | 0001
2802h + 0001h = 2803h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
IX | 0002
2802h + 0002h = 2804h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
IX | 0003
2802h + 0003h = 2805h

## Slide 23: 9. Base Register Addressing Mode
In base register addressing mode, contents of base register is added to address part of instruction to obtain effective address.
It is similar to the indexed addressing mode except the register now is called as base instead of index.
The base register hold the beginning/base address.
The address part of instruction holds the offset.
Offset remains same, the base changes.
When the offset is added to the base register the resultant number is the memory location where the operand will be placed.

## Slide 24: 9. Base Register Addressing Mode
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
Base | 2800
Offset= 0001h
Effective address of operand = Base Register + offset
2800h + 0001h = 2801h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2801h + 0001h = 2802h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2802h + 0001h = 2803h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2803h + 0001h = 2804h
Base | 2801
Base | 2802
Base | 2803

## Slide 25: 9. Base Register Addressing Mode
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
Base | 2800
Offset= 0003h
Effective address of operand = Base Register + offset
2800h + 0003h = 2803h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2801h + 0003h = 2804h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2802h + 0003h = 2805h
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2803h + 0003h = 2806h
Base | 2801
Base | 2802
Base | 2803

## Slide 26: 10. Autoincrement or Autodecrement Addressing Mode
It is similar to register indirect addressing mode.
Here the register is incremented or decremented before or after its value is used.

## Slide 27: 10. Autoincrement or Autodecrement Addressing Mode
1st Time
2nd Time
3rd Time
4th Time
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
HL | 2802
At start:
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
HL | 2803
HL | 2804
HL | 2805
HL pair incremented after its value is used
HL | 2802

## Slide 28: 10. Autoincrement or Autodecrement Addressing Mode
1st Time
2nd Time
3rd Time
4th Time
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
HL | 2803
At start:
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
2807 | 22
2806 | FF
2805 | 6D
2804 | 59
2803 | 08
2802 | 2E
2801 | F3
2800 | 9F
HL | 2805
HL | 2806
HL | 2807
HL pair incremented before its value is used
HL | 2804

## Slide 29: Example problem
Memory
Address
200
201
202
399
500
600
702
Load to AC | Mode
Address = 500 | 
Next Instruction | 
400 | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
PC | 200
R1 | 400
XR | 100
AC
800
PC = Program Counter R1 = Register
XR = Index Register AC = Accumulator
Memory is having first instruction to load AC
Mode will specify the addressing mode to get operand.
Address field of instruction is 500.
Find out the effective address of operand and operand value by considering different addressing modes.

## Slide 30: Example problem
Address Memory
200
201
202
399
400
500
600
702
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
PC | 200
R1 | 400
XR | 100
AC
800
1. Immediate Addressing Mode
As instruction contains immediate number 500.
It is stored as address 201.
Effective Address = 201
Operand = 500
AC | 500

## Slide 31: Example problem
Memory
Address
200
201
202
399
400
500
600
702
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
PC | 200
R1 | 400
XR | 100
AC
800
2. Register Addressing Mode
Register R1 contains 400.
As operand is in register so no any memory location.
Effective Address = Nil
Operand = 400
AC | 400

## Slide 32: Example problem
Memory
Address
200
201
202
399
400
500
600
702
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
PC | 200
R1 | 400
XR | 100
AC
800
3. Register Indirect Addressing Mode
Register R1 contains 400.
So effective address of operand is 400.
The data stored at 400 is 700.
Effective Address = 400
Operand = 700
AC | 700

## Slide 33: Example problem
Memory
Address
200
201
202
399
400
500
600
702
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
PC | 200
R1 | 400
XR | 100
AC
800
4. Direct Addressing Mode
Instruction contains the address 500.
So effective address of operand is 500.
The data stored at 500 is 800.
Effective Address = 500
Operand = 800
AC | 800

## Slide 34: Example problem
Memory
Address
200
201
202
399
400
500
600
702
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
PC | 200
R1 | 400
XR | 100
AC
800
5. Indirect Addressing Mode
Instruction contains the address 500.
Address at 500 is 800.
So effective address of operand is 800.
The data stored at 800 is 300.
Effective Address = 800 Operand = 300
AC | 300

## Slide 35: Example problem
Memory
Address
200
201
202
399
400
500
600
702
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
PC | 200
R1 | 400
XR | 100
AC
800
6. Relative Addressing Mode
PC = 200.
Offset = 500.
Instruction is of 2 bytes.
So effective address = PC + 2 + offset = 200 + 500 +2 = 702 .
The data stored at 702 is 325.
Effective Address = 702 Operand = 325
AC | 325

## Slide 36: Example problem
Memory
Address
200
201
202
399
400
500
600
702
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
PC | 200
R1 | 400
XR | 100
AC
800
7. Index Addressing Mode
XR = 100.
Base = 500.
So effective address = Base + XR = 500 + 100 = 600 .
The data stored at 600 is 900.
Effective Address = 600 Operand = 900
AC | 900

## Slide 37: Example problem
Memory
Address
200
201
202
399
400
500
600
702
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
PC | 200
R1 | 400
XR | 100
AC
800
8. Autoincrement Addressing Mode
It is same as register indirect addressing mode except the contents of R1 are incremented after the execution.
R1 contains 400.
So effective address of operand is 400.
The data stored at 400 is 700.
Effective Address = 400 Operand = 700
AC | 700
R1 | 401

## Slide 38: Example problem
Memory
Address
200
201
202
399
400
500
600
702
Load to AC | Mode
Address = 500 | 
Next Instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
PC | 200
R1 | 400
XR | 100
AC
800
9. Autodecrement Addressing Mode
It is same as register indirect addressing mode except the contents of R1 are decremented before the execution.
R1 contains 400.
R1 is first decremented to 399.
So effective address of operand is 399.
The data stored at 399 is 450.
Effective Address = 399 Operand = 450
AC | 450
R1 | 399